The Latest Developments in the X51A and X37B
by John M. DiIorio
May 17, 2013

---
● Definition
● Definition
- The Boeing X-51 (also known as X-51 WaveRider) is an unmanned scramjet demonstration aircraft for hypersonic (Mach 6, approximately 4,000 miles per hour [6,400 km/h] at altitude) flight testing.
- General characteristics:
  - Crew: None
  - Length: 25 ft in (7.62 m)
  - Empty weight: 4,000 lb (1,814 kg)
- Performance:
  - Maximum speed: Mach 6+ (3,600+ mph;
5,800+ km/h)
  - Range: 460 miles (740 km)
  - Service ceiling: 70,000 ft (21,300 m)
- Fuel:
  - Scramjet engine lighting: ethylene
  - Main propulsion: JP-7
- Control:
  - Four aerodynamically controlled fins
  - Autonomous control (external)
  - Recovery at sea (One is left)
The X51A under a B-52 wing

---
● History – Four (4) units were built
● History – Four (4) units were built
First Flight
  - May 26, 2010
  - Mach 5 at 70,000 feet for 200 seconds
  - Success
- Second Flight
  - March 24, 2011
  - Did not transfer to JP-7 fuel
  - Failure
- Third Flight
  - August 14, 2012
  - Upper right fin unlocked
  - Failure
- Fourth Flight
  - May 1, 2013
  - Mach 5.1 at 70,000 feet for 240 seconds
  - Success

---
● X51A Endgame
● X51A Endgame
Scramjet Demonstration Vehicle - March 24, 2011
X41 Falcon Mach 7-9
XJET Mach 6
X51 VLS (Sub)

---
● The Boeing X-37 (X-37 Orbital Test Vehicle)
● The Boeing X-37 (X-37 Orbital Test Vehicle)
The Boeing X-37 (X-37 Orbital Test Vehicle) is an American reusable unmanned spacecraft. It is boosted into space by a rocket, then re-enters Earth's atmosphere and lands as a spaceplane. The X-37 is operated by the U. S. Air Force for orbital spaceflight missions intended to demonstrate reusable space technologies.
General characteristics:
- Crew: None
- Length: 29 ft 3 in (8.9 m)
- Wingspan: 14 ft 11 in (4.5 m)
- Height: 9 ft 6 in (2.9 m)
- Loaded weight: 11,000 lb (4,990 kg)
- Powerplant: 1 Aerojet AR2-3 engine (hydrazine),
- 6,600 lbf (29.3 kN)
- Power: Gallium arsenide solar cells
- with lithium-ion batteries
- Payload bay: 7 ft × 4 ft (2.1 m × 1.2 m)
Performance:
- Orbital speed: 28,044 km/h (17,426 mph)
- Orbit: Low Earth orbit
- Orbital time: 270 days (design)
- Fuel: JP-8
Control:
Autonomous control (external) Self-Guided Landing

---
● History – Two (2) units were built
● History – Two (2) units were built
The X37B (first unit) autonomous landing at Vandenberg AFB on December 3, 2010
First Flight (Unit 1)
  - April 22, 2010
  - Orbited at 255 miles for 224 days
  - Success
- Second Flight (Unit 2)
  - March 5, 2011
  - Orbited at 255 miles for 469 days
  - Success
- Third Flight (Unit 1)
  - December 11, 2012
  - In orbit

---
● X37B Endgame
● X37B Endgame
Space Junk Vehicle
Cargo Space Transfer
X37C (E1, E2, L1)
Reusable Long-term Orbital Vehicle